## Slide 1
Layer 3 and the Internet Protocol (IP)
Tahir Azim
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Outline
Layer 3 (The Network Layer)
IP: The Internet Protocol
  Service characteristics
  IP addresses
  Fragmentation
  The IP Datagram format
  Classless Interdomain Routing (CIDR)
  An aside: Turning names into addresses (DNS)
  Forwarding IP Datagrams
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Layer 3 (The Network Layer)
Transports packets from sending to receiving host
On sending side, encapsulates packets into datagrams
On receiving side, delivers the packet to the transport layer
Network layer protocols run on every host and router in the path
Each router examines header fields in all IP datagrams passing through it

## Slide 4: Key Network-Layer functions
Forwarding
  Move packets from router’s input to appropriate router output
Routing
  Determine path taken by packets to go from sender to receiver
  “Routing algorithms”: run at routers to determine paths
  Routers have “forwarding tables”
    Based on destination address in datagram networks

## Slide 5: The Internet Protocol (IP)
App
Transport
Network
Link
TCP / UDP
IP
Data
Hdr
Data
Hdr
TCP Segment
IP Datagram
Protocol Stack
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: The Internet Protocol (IP)
Characteristics of IP
  CONNECTIONLESS: mis-sequencing
  UNRELIABLE: may drop packets…
  BEST EFFORT: … but only if necessary
  DATAGRAM: individually routed
A
R1
R2
R4
R3
B
Source
Destination
D
H
D
H
Architecture
Links
Topology
Transparent
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Fragmentation
A
Ethernet
MTU=1500 bytes
MTU=1500 bytes
B
Source
Destination
MTU<1500 bytes
Problem: A router may receive a packet larger than the maximum transmission unit (MTU) of the outgoing link.
R1
R2
Solution: R1 fragments the IP datagram into mutiple, self-contained datagrams.
Data
HDR (ID=x)
Data
HDR (ID=x)
Data
HDR (ID=x)
Data
HDR (ID=x)
Offset>0
More Frag=0
Offset=0
More Frag=1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Fragmentation
Fragments are re-assembled by the destination host; not by intermediate routers.
To avoid fragmentation, hosts commonly use path MTU discovery to find the smallest MTU along the path.
Path MTU discovery involves sending various size datagrams until they do not require fragmentation along the path.
Most links use MTU>=1500bytes today.
Try: traceroute –f berkeley.edu 1500 and traceroute –f berkeley.edu 1501
(DF=1 set in IP header; routers send “ICMP” error message, which is shown as “!F”).
Bonus: Can you find a destination for which the path MTU < 1500 bytes?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Fragmentation Example
Can you tell why the data field is 3280 bytes rather than 3300?
Ref: tcpipguide.com

## Slide 10: IP Addresses
IP (Version 4) addresses are 32 bits long
Every interface has a unique IP address:
  A computer might have two or more IP addresses
  A router has many IP addresses
IP addresses are hierarchical
  They contain a network ID and a host ID
  E.g. Stanford addresses start with: 171.64…
IP addresses are assigned statically or dynamically (e.g. DHCP)
IP (Version 6) addresses are 128 bits long
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: The IP Datagram
Flags
vers
TTL
TOS
checksum
HLen
Total Length
ID
FRAG Offset
Protocol
SRC IP Address
DST IP Address
(OPTIONS)
(PAD)
<=64 KBytes
Offset within original packet
Hop count
http://tools.ietf.org/html/rfc791
http://www.networksorcery.com/enp/default0904.htm
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: IP Addresses
Originally there were 5 classes:
CLASS “A”
1
7
0
Net ID
Host-ID
CLASS “B”
10
Net ID
Host-ID
24
2
14
16
CLASS “C”
110
Net ID
Host-ID
3
21
8
CLASS “D”
1110
Multicast Group ID
4
28
CLASS “E”
11110
Reserved
5
27
A
B
C
D
0
232-1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: IP Addresses Examples
Class “A” address: www.mit.edu
  18.181.0.31
  (18<128 => Class A)
Class “B” address: mekong.stanford.edu
  171.64.74.155
  (128<171<128+64 => Class B)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: IP Addressing
Problem:
Address classes were too “rigid”. For most organizations, Class C were too small and Class B too big. Led to inefficient use of address space, and a shortage of addresses.
Organizations with internal routers needed to have a separate (Class C) network ID for each link.
And then every other router in the Internet had to know about every network ID in every organization, which led to large address tables.
Small organizations wanted Class B in case they grew to more than 255 hosts. But there were only about 16,000 Class B network IDs.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: IP Addressing
Two solutions were introduced:
Subnetting within an organization to subdivide the organization’s network ID.
Classless Interdomain Routing (CIDR) in the Internet backbone was introduced in 1993 to provide more efficient and flexible use of IP address space.
CIDR is also known as “supernetting” because subnetting and CIDR are basically the same idea.
Notes: <number>
<footer>
<header>
<date/time>